Series GL2 Paired Frameless Glasswall Specifications

Part 1 - General

1.01 DESCRIPTION

A.	General

1.	Furnish and install operable glass partitions and suspension system.  Provide all labor, materials, tools, equipment, and services for glass operable walls in accordance with provisions of contract documents.

1.02 RELATED WORK BY OTHERS

A.	Preparation of opening will be by General Contractor.  Any deviation of site conditions contrary to approved shop drawings must be called to the attention of the architect.

B.	All header, blocking, support structures, jambs, and track enclosures, as required in 1.04 Quality Assurance.

C.	Prepunching of support structure in accordance with approved shop drawings.

D.	Paint or otherwise finishing all trim and other materials adjoining head and jamb of the partitions.

1.03 SUBMITTALS

A.	Complete shop drawings are to be provided prior to fabrication indicating construction and installation details.  Shop drawings must be submitted within 60 days after receipt of signed contract.

1.04 QUALITY ASSURANCE

A.	Preparation of the opening shall conform to the criteria set forth per ASTM E557 Standard Practice for Architectural Application and Installation of Operable Partitions..

B.	Glass shall be clear tempered per ASTM C1048-97b.

1.05 PRODUCT DELIVERY, STORAGE, AND HANDLING

A.	Proper storage of partitions before installation and continued protection during and after installation will be the responsibility of the General Contractor.

1.06 WARRANTY.  Track, carriers, and horizontal rails shall be guaranteed for one year against defects in material and workmanship.  The glass is not included in this warranty.

Part 2 - Products

2.01 ACCEPTABLE MANUFACTURERS

A.	Upon compliance with all of the criteria specified in this section, Manufacturers wishing to bid products similar to the product specified must submit to the architect 10 days prior to bidding complete data in support of compliance and a list of three past installations of products similar to those listed.  The submitting manufacturer guarantees the proposed substituted product complies with the product specified and as detailed on the drawings.

2.02 MATERIALS

A.	Product to be top supported, center stacked, Series GL2 paired glass panels as manufactured by Hufcor.

1.	Panels shall be nominally 1-5/8” [40] thick and to 48” [1219] in width.

2.	Glass shall be mechanically attached to top and bottom rails and not rely on friction and/or adhesives.

3.	All glass edges shall be polished and glass panel faces shall be a choice of

a.	1/2” [12] fully tempered glass

b.	1/2” [12] laminated glass.

c.	1/2” satiny translucent acid washed, full height, one side only

d.	Optional (factory approval required):

Acrylic

Custom glass

4.	Top and bottom horizontal rail shall be anodized aluminum and incorporate brush light seals.

5.	Glass faces shall have no vertical trim.  (Important note:  there is a 1/4-1/2” [6-12] gap between panel joints to prevent glass from touching during panel setup. Size of gap varies due to glass tolerances.)  Optional upgrade:  Glass faces shall have vertical trim of clear anodized aluminum.

6.	Each panel contains a footbolt which is extended into a floor mounted receiver to stabilize and secure each panel in the opening.

B.	Weight of the panels shall be approximately 7.4 lbs. per sq. ft. for 1/2” [12] glass.

C.	Suspension system:

1.	Track shall be of clear anodized architectural grade extruded aluminum alloy 6063-T6.  Track design shall provide integral support for adjoining ceiling, soffit, or plenum sound barrier.  Track shall be connected to the structural support by min. 3/8” [10] dia. threaded steel hanger rods.  Guide rails and/or track sweep seals shall not be required.

a.	Each panel shall be supported by one 4-wheeled carrier.  Wheels to be of hardened steel ball bearings encased with molded polymer tires.

D.	Finishes

1.	Horizontal rail color shall be (select one):

a.	Clear anodized (standard)

b.	Medium Bronze anodized (optional upgrade)

c.	Dark Bronze anodized (optional upgrade)

d.	Stainless steel clad (optional upgrade)

#4 brushed

#8 mirrored

e.	Custom painted (optional upgrade)

f.	Powder coated (optional upgrade)

2.	Aluminum track shall be clear anodized

a.	Optional upgrade:

(1)	custom anodized

(2)	custom powder coated

E.	Available Accessories/Options

1.	Pivot panel closure

a.	Low profile handle (standard)

b.	Vertical tube handle with push/pull handle one or both sides(optional)

c.	Vertical tube handle with optional tube push bar, one side

2.	Locks

a.	Thumb turn floor lock

b.	Keyed floor lock

3	Glass etching

a.	Fully etched and sealed

b.	Custom patterns

2.03 OPERATION

A.	Panels shall be manually moved from the storage area, unfolded, positioned in the opening, and floorbolts set.

B.	Final partition closure to be by (select one):

1.	Pivot panel

2.	Overlapping the opening

3.	End at wall

C.	Stack/Store Panels

1.	Retract footbolts, fold, and move to storage area.  Panels may be stored at either or both ends of the track or in a pocket.

Part 3 - Execution

A.	Installation.  The complete installation of the glass wall system shall be by an authorized factory-trained installer and be in strict accordance with the approved shop drawings and manufacturer’s standard printed specifications, instructions, and recommendations.

B.	Cleaning

1.	All track and panel surfaces shall be wiped clean and free of handprints, grease, and soil.

2.	Optional specialty glass requires special cleaning per instructions provided.

3.	Cartoning and other installation debris shall be removed to onsite waste collection area.

C.	Training

1.	Installer shall demonstrate proper operation and maintenance procedures to owner’s representative.

2.	Owners manuals shall be provided to owner’s representative.